## Slide 1
Week2 Measuring Weight and Volume

## Slide 2
Purpose
Learn how to use scale and liquid transfer equipment, as well as how to process experimental data and estimate uncertainty

## Slide 3
Theory
Weight, Mass, Density, Volume
Liquid Volume Measurement Apparatus
Measurement of Solid Volume
Solubility, Melting Point
Error, Uncertainty
Significant Figures

## Slide 4
Chemicals & Apparatus
Chemicals
Name | Molecular formula | Molecular weight (g/mol) | Melting point(℃) | Boiling point(℃) | Density(g/cm3)
Water | H2O | 18.02 | 0 | 100 | 1
Hexane | C6H14 | 86.18 | -95.3 | 68.7 | 0.66
Methylene chloride(MC) | CH2Cl2 | 84.93 | -96.7 | 39.3 | 1.33
Biphenyl | C12H10 | 154.21 | 69.2 | 255 | 1.04
Acetamide | C2H5NO | 58.08 | 79-81 | 221.2 | 1.16
Acetone | C3H6O | 58.08 | -94.9 | 56.08 | 0.78
Aluminum | Al | 26.98 | 660.32 | 2470 | 2.70

## Slide 5
Chemicals & Apparatus
Apparatus
Experiment |  | 
A. Weight Measurement | Acetamide, Scale, Weighing Paper | 
B. Transferring Liquid Using a pipette | Scale, Distilled Water, Beaker(100mL) | Pipette (10mL), Pipette Filler
C. Transferring Liquid Using a Graduated cylinder |  | Graduated Cylinder (10mL)
D. Transferring Liquid Using a Buret |  | Buret (50mL), Stand, Clamp
E. Determining the Solubility of a Compound | Biphenyl, Acetamide | Test Tube , Distilled Water, Hexane
F. Determining the Melting Point of a Compound |  | Capillary Tube, Melting Point Apparatus
G. Determining the density of a Compound | Graduated cylinder (10mL), MC, Al, Hexane | 

## Slide 6
Procedure
A. Weight Measurement
1. Examine the measured capacity (maximum measured weight) and precision of the scale to be used in the experiment.
2. Measure the weight of 1g of acetamide.
< How to use the scale >
Place a weighing paper on the plate and tare the scale.
Check the mass when the scale reading remains stable for 3 seconds, and record it.

## Slide 7
Procedure
pipette
When taking liquid
When removing liquid
B. Transferring Liquid Using a pipette
Place the beaker on the scale and measure its weight.
(Repeat twice) Transfer 10 mL of distilled water into the beaker using a pipette and measure its weight.
Using the density of water, calculate the average volume and standard deviation (uncertainty) of the distilled water.

## Slide 8
Procedure
C. Transferring Liquid Using a Graduated cylinder
Place the beaker on the scale and measure its weight.
(Repeat twice) Transfer 10 mL of distilled water into the beaker using a graduated cylinder and measure its weight.
Using the density of water, calculate the average volume and standard deviation (uncertainty) of the distilled water.

## Slide 9
Procedure
Closed state
Open state
D. Transferring Liquid Using a Buret
Place the beaker on the scale and measure its weight.
(Repeat twice) Transfer 10 mL of distilled water into the beaker using a buret and measure its weight.
Using the density of water, calculate the average volume and standard deviation (uncertainty) of the distilled water.
When removing liquid

## Slide 10
Procedure
E. Determining the Solubility of a Compound
Add one small spatula scoop of acetamide into the test tube.
Add distilled water and n-hexane into the test tube to a height of 1–2 cm from the bottom.
Shake the test tube well for about 5 minutes and observe the state.
Record the experimental results as S (Soluble) or I (Insoluble).
Determine the solubility of biphenyl using the same method as in steps 1 to 4.

## Slide 11
Procedure
F. Determining the Melting Point of a Compound
Tap the melting point capillary tube into biphenyl 4 to 5 times *If the reagent is too clumpy, press and crush it with a spatula to fill the capillary tube.
Lightly tap the end of the capillary tube on the desk to help fill it with powder.
Place it in the melting point apparatus and measure the melting point.
Determine the melting point of acetamide using the same method as in steps 1 to 3.

## Slide 12
Procedure
G. Determining the density of a Compound
Check the density of methylene chloride (MC)
Place the graduated cylinder on the scale and measure its weight.
Fill the graduated cylinder with 10 mL of MC and measure its weight.
Check the density of aluminum
Weigh the two aluminum pieces.
Add 5 mL of n-hexane to the graduated cylinder, then place the two pieces of aluminum in it and measure the volume change. (Do not discard the aluminum)

## Slide 13
Data & Results
Maximum Measurement Weight | precision | Acetamide Weight
A. Weight Measurement
 | Group Member 1 | Group Member 2 | Average
The weight of 10 mL of distilled water |  |  | 
Actual volume of water (mL) |  |  | 
B. Transferring Liquid Using a pipette

## Slide 14
Data & Results
- 물의 밀도 = 0.99705 g/mL (25℃)
- 부피 불확정도 ≈ 0.027 mL
C. Transferring Liquid Using a Graduated cylinder
D. Transferring Liquid Using a Buret
 | Group Member 1 | Group Member 2 | Average
The weight of 10 mL of distilled water |  |  | 
Actual volume of water (mL) |  |  | 
 | Group Member 1 | Group Member 2 | Average
The weight of 10 mL of distilled water |  |  | 
Actual volume of water (mL) |  |  | 

## Slide 15
Data & Results
 | Water | n-Hexane
Acetamide |  | 
Biphenyl |  | 
E. Determining the Solubility of a Compound
 | Melting point measurement
A : Acetamide (79~81 °C) | 
B : Biphenyl (69.2 °C) | 
F. Determining the Melting Point of a Compound

## Slide 16
Data & Results
1) MC (Theoretical value : 1.33g/mL) | 13.353 g
Weight of 10 mL of MC | 
MC density experimental value | 
2) Aluminum (Theoretical value : 2.70g/mL) | 13.353 g
Al Weight | 
Volume change of n-Hexane | 
Al density experimental value | 
G. Determining the density of a Compound